SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 1 of 6

Building Name: St. Mary School

Building Address:  313 Tryon Street Woodstock, Illinois 60098

Name of Person Completing Report:

Title:						                       			Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 01 | 1’x1’ Ceiling Tile- Regular Pinholes | Elem School- Basement, 1st & 2nd Floor- Scattered Rooms Throughout | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 02 | 18”x18” Ceiling Tile- White | Elem School- Now (Main Office) | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 03 | 1’x1’ Ceiling Tile- White | Elem School- Room E102 | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988- Material No Longer in Building |
| 04 | Gypsum Ceiling | Elem School- Basement | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 05 | 1’x1’ Ceiling Tile/Adhesive*- Irregular | Elem School- E201 | ND | ND |  | Ceiling Tile Material Analyzed to be NON-ACM in 1988- * Adhesive is ASSUMED |
| 06 | 12”x12” Floor Tile/Mastic- Off-White | Elem School- 1st & 2nd Floor Stairwell | ND | ND |  | Tile Negative in 1988 by PLM-Both Tile and Mastic to remain ASSUMED- analyze Tile by TEM Method |
| 07 | 12”x12” Floor Tile/Mastic- Off-White w/Green | Elem School Auditorium Under Carpet | ND | ND |  | Tile analyzed TEM 14% Chrysotile by TNC in 2018 Mastic Analyzed to be NON-ACM by TNC in 2018 |
| 08 | 12”x12” Floor Tile/Mastic- Tan w/Brown Marks | Elem School- Basement- Library | ND | ND |  | Preventive Measures… Continue O&M- Mastic is ASSUMED |
| 09 | 12”x12” Floor Tile- Brown | N/A | N/A | N/A |  | Material Removed/Abated |
| 10 | 9”x9” Floor Tile/Mastic- Green | Elem School- Basement NW Storage Room | ND | ND |  | Preventive Measures… Continue O&M- Mastic is ASSUMED encapsulated under Sakrete |
| 11 | Air Cell Pipe Insulation | Elem School- Storage Behind Bathrooms, Throughout Inaccessible Areas | ND | ND |  | Preventive Measures… Continue O&M |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.  NOTE:   If the status of the ACBM has changed, then photograph the area and record the photograph number in the space provided.  Notify the Asbestos Program Manager immediately concerning any changes.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 2 of 6

Building Name: St. Mary School

Building Address:  313 Tryon Street Woodstock, Illinois 60098

Name of Person Completing Report:

Title:							                     		Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 12 | Boiler Insulation | Elem School Boiler Room | N/A | N/A |  | Material Removed/Abated in June 1989 |
| 13 | 9”x9” Floor Tile/Mastic- White w/Black Streaks & Red Tiles | Jr. High- Main Office, Principal’s Office, Rooms 101 (under MFE), 102,201 | ND | ND |  | Preventive Measures… Continue O&M- Mastic is ASSUMED |
| 14 | 9”x9” Floor Tile/Mastic- Dark Brown & White | Jr. High- Room 203 (under MFE) | ND | ND |  | Preventive Measures… Continue O&M- Mastic is ASSUMED |
| 15 | 9”x9” Floor Tile/Mastic- Brown & Red | Jr. High- Room 202 (under MFE) 2nd Floor- Hallway, West Storage Room | ND | ND |  | Preventive Measures… Continue O&M- Mastic is ASSUMED |
| 16 | 9”x9” Floor Tile/Mastic- Brown & Dark Brown | Jr. High- Room 301 (under MFE) | ND | ND |  | Preventive Measures… Continue O&M- Mastic is ASSUMED |
| 17 | 1’x1’ Ceiling Tile/Adhesive | Throughout | N/A | N/A |  | Tile Analyzed to be NON-ACM in 1988- Adhesive Analyzed by MEC to be NON-ACM in Oct 2012 |
| 18 | Pipe Insulation | Jr. High- Tunnels & Throughout School | ND | ND |  | Preventive Measures… Continue O&M- Material Removed/Abated from Boiler Room in April 1998- |
| 19 | Boiler Insulation | Jr. High- Boiler Room | N/A | N/A |  | Material Removed/Abated from Boiler Room in April 1998 |
| 20 | 1’x1’ Ceiling Tile/Adhesive (Adhesive is Designated as HA# MMB) | Cafeteria | ND | ND |  | Adhesive sampled by MEC Analyzed Positive- Oct 2012- Tile (HA# 20) Positive with Adhesive on it |
| 21 | 1’x1’ Ceiling Tile- Rough | Kitchen | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988- No Adhesive found for this Material |
| 22 | Gypsum Wall Board | Elem School- Cafeteria-Mechanical Rooms | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.  NOTE:   If the status of the ACBM has changed, then photograph the area and record the photograph number in the space provided.  Notify the Asbestos Program Manager immediately concerning any changes.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 3 of 6

Building Name: St. Mary School

Building Address:  313 Tryon Street Woodstock, Illinois 60098

Name of Person Completing Report:

Title:						                       			Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 23 | Linoleum- Black | Jr. High- Basement- Storage Rooms | ND | ND |  | Preventive Measures… Continue O&M |
| 24,25,26A,26B,27 | Mastics-Various | Elem & Jr. High Buildings | N/A | N/A |  | HA# 24,25,26A,26B,27 have been Eliminated and are now Included w/Individual Associated Tiles |
| 28 | Vibration Damper | Cafeteria- Mechanical Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M |
| 29 | Plaster | Jr. High- Throughout | N/A | N/A |  | Material Analyzed by MEC to be NON-ACM in 2012 |
| 30 | Plaster | Elem School- Throughout | N/A | N/A |  | Material Analyzed by MEC to be NON-ACM in 2012 |
| MBA | Vinyl Wall Base/Mastic- Brown | Jr. High- Stairwells & Basement Bathroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MCA | 2’x4’ Lay-In Ceiling Tile- Fissures & Pinholes | Jr. High- 2nd Floor- Girl’s Bathroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MCB | 2’x4’ Acoustical Ceiling Board | Jr. High- 1st Floor North Foyer | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MCC | 1’x1’ Ceiling Tile/Adhesive- Large Holes | Jr. High- Cafeteria- SE Storage Areas & Girl’s Bathroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFA | Terrazzo- Black, Brown & Gray | Jr. High- Hallways & Stairs | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFB | Terrazzo- Black, Beige & Tan Stone Pattern | Jr. High- Room 103 | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.  NOTE:   If the status of the ACBM has changed, then photograph the area and record the photograph number in the space provided.  Notify the Asbestos Program Manager immediately concerning any changes.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 4 of 6

Building Name: St. Mary School

Building Address:  313 Tryon Street Woodstock, Illinois 60098

Name of Person Completing Report:

Title:						                       			Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MFC | Terrazzo- Black, Beige & Tan Stone Pattern | Jr. High- 1st Floor- North Foyer & East Entrance Foyer | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFD | Linoleum- Wood Pattern | Jr. High- Principal’s Office | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFE | 12”x12” Floor Tile/Mastic- Beige w/Gray Flecks | Jr. High- Rooms 102,202,203,301 | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFF | 12”x12” Floor Tile/Mastic- Beige w/Purple, Blue & Gray Flecks | Jr. High- Main Office | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFG | 1”x1” Ceramic Tile/Grout- Hexagon Pattern | Jr. High- Boy’s & Girl’s Gym Locker Rooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFH | Terrazzo- Pink, Black & White Stone Pattern | Jr. High- Cafeteria | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MMA | Puck Adhesives (Associated w/HA# 17*) | Jr. High- 1st & 2nd Floor Classrooms | N/A | N/A |  | *Tile Analyzed to be NON-ACM in 1988- Adhesive Analyzed by MEC to be NON-ACM in Oct 2012 Material Identified by MEC in 2012 |
| MMB | Puck Adhesive (Associated w/HA# 20) | Jr. High- Cafeteria | ND | ND |  | Adhesive sampled by MEC Analyzed Positive- Oct 2012- Tile (HA# 20) Positive with Adhesive on it Material Identified by MEC in 2012 |
| MDA | Gypsum Ceiling | Jr. High- Cafeteria | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M NOTE: Positive Ceiling Tile Adhesive is Glued to Gypsum- Material Identified by MEC in 2012 |
| MDB | Drywall w/Compound & Tape | Jr. High- Cafeteria- West Storage Rooms & Hall | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MBA | 6” Vinyl Wall Base/Mastic- Green | Elem School- 2nd Floor- Hall-Storage, SW Stairwell | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 5 of 6

Building Name: St. Mary School

Building Address:  313 Tryon Street Woodstock, Illinois 60098

Name of Person Completing Report:

Title:						                       			Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MBB | Vinyl Wall Base/Mastic- Black | Elem School- Basement- Bathrooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFA | 12”x12” Floor Tile/ Mastic- Gray w/White & Dark Gray Flecks | Elem School- Stairwells, Basement Bathrooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFB | 12”x12” Floor Tile/Mastic- Dark & Light Flecks | Elem School- Basement- Art Room & Hall | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFC | 1”x1” Ceramic Tile/Grout- Light & Dark Green | Elem School- Basement- Girl’s Bathroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFD | 1”x1” Ceramic tile/Grout- White w/Brown Tile Border | Elem School- 1st Floor- Hallway/Foyer | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFE | Linoleum- Green | Elem School- Stairwells | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFG | 12”x12” Floor Tile/Mastic- Beige w/Gray Flecks | Elem School- Basement- Pre-School Classroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFH | 12”x12” Floor tile/Mastic- Light Gray w/Gray White Flecks | Elem School- 1st Floor- Copy Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MMA | Boiler Gasket | Elem School- Boiler Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MMC | Puck Adhesive Associated w/HA# 01 | Elem School- Basement, 1st & 2nd Floor- Scattered Rooms Throughout | N/A | N/A |  | Material Analyzed by MEC to be NON-ACM in 2012 Material Identified by MEC in 2012 |
| SCA | Stucco Ceiling | Elem School- Basement- Pre-School Classroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.  NOTE:   If the status of the ACBM has changed, then photograph the area and record the photograph number in the space provided.  Notify the Asbestos Program Manager immediately concerning any changes.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 6 of 6

Building Name: St. Mary School

Building Address:  313 Tryon Street Woodstock, Illinois 60098

Name of Person Completing Report:

Title:						                       			Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MFI | 1”x1” Ceramic Tile/Grout- White | Elem School- Basement Boy’s Bathroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2015 |
| MMC | Wood Floor Mastic | Jr High- Gymnasium Floor | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2015 |
| MCD | 2’x4’ Ceiling Tiles-2’x2’ Squares w/Pin Holes & Fissures | Music Room, Tech Room | N/A | N/A |  | Armstrong Letter on File Material Identified by True North in 2018 |
| MMD | Drywall Joint & Compound | Music Room, Tech Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2018 |
| MBC | 4” Baseboard/Adhesive- Gray | Music Room, Tech Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2018 |
| MFJ | 12”x12” Floor Tile/Mastic- Gray w/Gray Marks | Music Room, Tech Room, Hallway, Bathroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2018 |
| MWA | 2”x2” Ceramic Tile/Grout- White | Music Room, Tech Room, Bathroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2018 |
| MFK | 12”x12” Ceramic Tile/Grout- Gray | Stairway and Landing to Music Room and Tech Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2018 |
| MFL | Sheet Flooring- Black | Stairway to Music Room and Tech Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2018 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.  NOTE:   If the status of the ACBM has changed, then photograph the area and record the photograph number in the space provided.  Notify the Asbestos Program Manager immediately concerning any changes.