SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 1 of 4

Building Name: St. Andrew

Building Address:  701 Eleventh Avenue Rock Falls, Illinois 61071

Name of Person Completing Report:

Title:  			                       					       Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 01 | Air Cell Pipe Insulation | Throughout Building | ND | ND |  | Preventive Measures… Continue O&M- Material Abated from Boiler Room in 1989, from South Tunnel 2014- from Grade 2 to Office and Tunnels sealed… Boiler permanently shut down-2015 |
| 02 | HA#02 Not Used In Original Inspection | HA#02 Not Used In Original Inspection | N/A | N/A |  | HA#02 Not Used In Original Inspection |
| 03 | Tank Insulation | Boiler Room | N/A | N/A |  | Material Removed/Abated in 1989 |
| 04 | Boiler Insulation | Boiler Room | N/A | N/A |  | Material Removed/Abated in 1989 |
| 05 | Boiler Gasket | Boiler Room | N/A | N/A |  | Material Removed/Abated in 1989 |
| 06 | Boiler Breeching | Boiler Room | N/A | N/A |  | Material Removed/Abated in 1989 |
| 07 | Plaster Ceiling | Classrooms & Hallways | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 08 | 2’x2’ Ceiling Tile- | Gymnasium | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 09 & SCB | Spray Applied Ceiling | Storage, East Pre-K Classrooms | ND | ND |  | Preventive Measures… Continue O&M |
| 10 | Plaster Walls | Walls Throughout Building | N/A | N/A |  | Analyzed by True North to be NON-ACM in 2015 |
| 11 | Gypsum Wall Board | East Pre-k Classrooms, Storage, Teacher’s Lounge | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 2 of 4

Building Name: St. Andrew

Building Address:  701 Eleventh Avenue Dixon, Illinois 61071

Name of Person Completing Report:

Title:					                       		    		 Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 12 | 9”x9” Floor Tile/Mastic- Brown w/Red & White Streaks | 1st Floor- Classrooms & Hallways | ND | ND |  | Preventive Measures… Continue O&M- Mastic is ASSUMED Flooring covered with new flooring |
| 13 | 9”x9” Floor Tile/Mastic- Green w/White & Tan Flecks | East Pre-K Classrooms & Hall to Mobile Classroom | ND | ND |  | Tile Negative in 1988 by PLM-Both Tile and Mastic to remain ASSUMED- analyze Tile by TEM Method Flooring covered with new flooring |
| 14 | 9”x9” Floor Tile- Off-White | Kitchen Storage, East Pre-K Classroom | N/A | N/A |  | Material Removed/Abated- HA# 13 & HA# MFA now Located in these Areas |
| 15 | Rubberized Flooring | Gymnasium | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 16 | Lay-In Insulation | Attic Above Gym | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 17 | Cardboard Pipe Insulation | Boiler Room, Pipe Tunnels Throughout | ND | ND |  | Preventive Measures… Continue O&M Material Abated from Boiler Room in 1989- |
| 18 & SCA | Spray Applied Ceiling Material | 1st Floor Throughout | ND | ND |  | Preventive Measures… Continue O&M |
| 19 | 9”x9” Floor Tile Mastic | Throughout | N/A | N/A |  | HA# 19 has been Eliminated and is now Included w/Individual Associated Tiles |
| 20 | Air Cell Pipe Fittings Insulation | Throughout | N/A | N/A |  | HA# 20 Descriptions have been Eliminated and is now Included w/HA# 01 |
| SCA | Stucco Ceiling | Original Building- 1st Floor Throughout | N/A | N/A |  | Included with HA #18 Identified by MEC in 2012 |
| SCB | Stucco Ceiling | East Pre-K Classrooms, Kitchen Storage, Entrance Foyer, Library | N/A | N/A |  | Included with HA #9 Identified by MEC in 2012 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 3 of 4

Building Name: St. Andrew

Building Address:  701 Eleventh Avenue Rock Falls, Illinois 61071

Name of Person Completing Report:

Title:  					                       				Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MDA | Drywall Ceiling w/Compound & Tape | Basement- Storage Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 |
| MDB | Drywall Ceiling | Kitchen Storage Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 |
| MDC | Textured Drywall Ceiling | 6-8th Grade Mobile Classrooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 |
| MBA | Vinyl Wall Base/Mastic- Brown | Classrooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 |
| MBB | Vinyl Wall Base/Mastic- Black | South Pre-K Classroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 |
| MBC | Vinyl Wall Base/Mastic- Gray | North Pre-K, K Classroom, 6-8th Grade Mobile Classroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 |
| MBD | Vinyl Wall Base/Mastic- Beige | Boy’s & Girl’s Bathrooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 |
| MMA | Fire Door | Boiler Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 |
| MFA | 12”x12” Floor Tile/Mastic- Beige w/Tan Flecks | Kitchen Storage, East Pre-K Classroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M True North-NEG by PLM-2015 confirm by TEM Identified by MEC in 2012 Flooring covered with new flooring |
| MFB | 12”x12” Floor Tile/Mastic- Gray w/Dark Gray & White Flecks | 6-8th Grade Classroom including Vestibule | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 Flooring covered with new flooring |
| MFC | 12”x12” Floor Tile/Mastic- Beige w/Dark Gray Flecks | Boy’s & Girl’s Bathrooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 Flooring covered with new flooring |

*** Material Condition***

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 4 of 4

Building Name: St. Andrew

Building Address:  701 Eleventh Avenue Rock Falls, Illinois 61071

Name of Person Completing Report:

Title:  				                       					Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MFD | 12”x12” Floor Tile/Mastic- Gray & Beige Flecks | Entry Foyer | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M- Neg. by PLM by True North 2015, Confirm by TEM Identified by MEC in 2012 |
| MCA | 1’x1’ Ceiling Tile- Smooth | Vestibule to 6-8th Grade Mobile Classroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by MEC in 2012 |
| MBE | 6” Vinyl Wall Base- Black | 4th Grade Classroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Identified by True North in 2015 |
| SCC | Stucco Ceiling & Plaster- White | Main Entrance, Library | N/A | N/A |  | Analyzed by True North to be NON-ACM in 2015 Identified by True North in 2015 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each year.