SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 1 of 5

Building Name: Holy Family School

Building Address:  4407 Highcrest Road Rockford, Illinois 61107

Name of Person Completing Report:

Title:					                       				Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 01 | 9”x9” Floor Tile- Olive w/White Specks | Cafeteria, Stairwells, 2nd Floor Hallways | N/A | N/A |  | Material Removed/Abated |
| 02 | 9”x9” Floor Tile- Tan w/Brown & White Streaks | 101,102,103,104,106,109, 201,202,203,208,211, Teachers’ Lounge, Office, Gym Upper Level | N/A | N/A |  | Material could not be located anywhere in facility on 8-7-2012. SEE HA# MFB for newly identified Tile Original Mastic Identified as HA# 14 |
| 03 | HA# 3 Not Used in Original Inspection | HA# 3 Not Used in Original Inspection | N/A | N/A |  | HA# 3 Not Used in Original Inspection |
| 04 | 9”x9” Floor Tile-Light Tan w/White Streaks | 2nd Floor- | N/A | N/A |  | Material could not be located anywhere in facility on 8-7-2012. SEE HA# MFB for newly identified Tile |
| 05 | 2’x2’ Ceiling Tile- Pin Holes & Gouges | Halls, Stairwells | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 06 | 2’x4’ Ceiling Tile- Pin Holes & Gouges | Classrooms109,206,209,Nurses Office | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 07 | Plaster Walls & Ceilings | Classrooms, Halls, Bathrooms | N/A | N/A |  | 3 Samples NON-ACM in 1988- Additional Negative samples in Dec 2009 to satisfy required sampling |
| 08 | Gypsum Board | Art Room | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 09 | 2’x2’ Ceiling Tile- Pitted | Copy Room, 1st Floor, Basement | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 10 | 2’x2’ Ceiling Tile- Various Holes | Cafeteria, Library, Kindergarten | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 11 | Hot Water Tank Insulation | Boiler Room | N/A | N/A |  | Material Removed/Abated |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.  NOTE:   If the status of the ACBM has changed, then photograph the area and record the photograph number in the space provided.  Notify the Asbestos Program Manager immediately concerning any changes.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 2 of 5

Building Name: Holy Family School

Building Address:   4407 Highcrest Road Rockford, Illinois 61107

Name of Person Completing Report:

Title:					                       				Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 12 | Steam & Water Pipe Insulation | Boiler Room, above Ceilings, Mechanical Rooms | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 13 | Pipe Fitting Insulation | Throughout School | ND | ND |  | Preventive Measures… Continue O&M- abated from Gym closet 3-4-16 abated from Water Main Closet 3-30-16, Repaired in Bathroom chases: May, 2018. Boiler Room Abated May, 2018. |
| 14 | 9”x9” Floor Tile Mastic | Classrooms, Gym Balcony, Office Area, Teacher’s Lounge | ND | ND |  | Preventive Measures… Continue O&M- *Mastic is assumed to be remaining under new Tile |
| 15A | 9”x9” Floor Tile- | Room 109 | N/A | N/A |  | This HA# has been eliminated- All 9x9 Tile types have been reclassified under HA# MF_’s |
| 15B | 9”x9” Floor Tile Mastic (Associated w/HA# 15A) | Room 109 | N/A | N/A |  | This HA# has been eliminated- All 9x9 Mastic types have been reclassified under HA# MF_’s |
| 16 | Cementitious Pipe Fitting | Room 103, Gym Changing Room | N/A | N/A |  | This HA# has been eliminated- Material is now included w/HA# 13 |
| 17 | Plaster | Gymnasium | N/A | N/A |  | Material Analyzed by INTEGRITY to be NON-ACM in December 2009 |
| 18 | Drywall & Joint Compound | Stairwell and Gym | N/A | N/A |  | Analyzed by True North to be NON-ACM in 2018 |
| 19 | Vibration Damper | Mechanical Rooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M |
| MFA | Terrazzo- Brown Stone Pattern | Basement Hall, 1st Fl Hall, Gym-1st Fl Hall, 2nd Fl Boy’s & Girl’s Locker Rms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFB | 12”x12” Floor Tile/Mastic- Beige & Gray Flecks | Kitchen, 1st Fl- Offices, Server Rm, Lounge, 2nd Fl- 207A,207B,209, Bathroom & Hall- West End | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M-Original Mastic may be Present under Existing Tile Material Identified by MEC in 2012 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Prop. Mgr.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 3 of 5

Building Name: Holy Family School

Building Address:  4407 Highcrest Road Rockford, Illinois 61107

Name of Person Completing Report:

Title:					                       				Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MFC | 9”x9” Floor Tile/Mastic- Tan w/White Streaks | 1st fl-101,102,104,106,109 2nd floor- 201,202,203,208 Gym- 2nd floor Hallway | ND | ND |  | Mastic Analyzed by True North to be ACM in 2018- Tile TEM/NEG- Preventive Measures… Continue O&M- Material Identified by MEC in 2012 |
| MFD | 9”x9” Floor Tile/Mastic- Dark Tan w/White Streaks | Classroom 206 | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M-Original Mastic may be Present under Existing Tile Material Identified by MEC in 2012 |
| MFE | 12”x12” Floor Tile/Mastic- Tan w/Multi Brown Flecks | Basement- Cafeteria, LL5 1st floor 103,108 2nd floor- 204,205,Hallway | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M-Original Mastic may be Present under Existing Tile Material Identified by MEC in 2012 |
| MFF | 1”x2” & 2”x2” Ceramic Tile/Grout- Light Blue, Dark Blue & White | Basement- LL2 1st & 2nd floor Boy’s Bathrooms | N/A | N/A |  | Analyzed by True North to be NON-ACM in 2018 Material Identified by MEC in 2012 |
| MFG | 1”x2” & 2”x2” Ceramic Tile/Grout- Light Green, Dark Green & White | Basement- LL4 1st & 2nd floor Girl’s Bathrooms | N/A | N/A |  | Analyzed by True North to be NON-ACM in 2018 Material Identified by MEC in 2012 |
| MFH | Linoleum- Brown w/White & Pink Streaks | Center Stairwell | ND | ND |  | Analyzed by True North to be NON-ACM in 2018 Material Identified by MEC in 2012 |
| MFI | 12”x12” Floor Tile/Mastic- Narrow Tan w/Multi Brown Flecks | Rooms 204,211 Gym- 2nd Floor Hallway & Girl’s Locker Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFJ | 12”x12” Floor Tile/Mastic- Beige w/Gray Flecks | Basement- Cafeteria, Entry Foyer to Bathrooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFK | 2”x2” Ceramic Tile/Grout- Gray | Basement- Cafeteria, Boy’s & Girl’s Bathrooms | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MFL | Linoleum- Brown | Cafeteria, Stairs | ND | ND |  | Analyzed by True North to be NON-ACM in 2018 Material Identified by MEC in 2012 |
| MFM | Linoleum- Tan w/White Streaks | Gym- Stairs to 2nd Floor, East Stairwell | ND | ND |  | Analyzed by True North to be ACM in 2018 Material Identified by MEC in 2012 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 4 of 5

Building Name: Holy Family School

Building Address:   4407 Highcrest Road Rockford, Illinois 61107

Name of Person Completing Report:

Title:					                       				Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MFN | 1”x1” Ceramic Tile/Grout-Green | 2nd Floor Boy’s Bathroom | N/A | N/A |  | Analyzed by True North to be NON-ACM in 2018 Material Identified by MEC in 2012 |
| MBA | Vinyl Wall Base/Mastic-Tan | Basement- Cafeteria 2nd Floor- 207A,207B,209 | N/A | N/A |  | Analyzed by True North to be NON-ACM in 2018 Material Identified by MEC in 2012 |
| MBB | 6” Vinyl Wall Base/Mastic- Tan | Cafeteria & Kitchen Area | N/A | N/A |  | Analyzed by True North to be NON-ACM in 2018 Material Identified by MEC in 2012 |
| MCA | 2’x2’ Convex Lay-In Ceiling Tile- Pin Holes | Room LL5 | N/A | N/A |  | Material Analyzed by MEC to be NON-ACM in August 2012 Material Identified by MEC in 2012 |
| MCB | 2’x4’ Lay-In Ceiling Tile- Gypsum | Kitchen | N/A | N/A |  | Material Analyzed by MEC to be NON-ACM in August 2012 Material Identified by MEC in 2012 |
| TTA | Tank Insulation | Boiler Room | N/A | N/A |  | Material Identified by MEC in 2012 Removed/Abated May 2018. |
| MMA | Boiler Gasket Rope | Boiler Room | N/A | N/A |  | Material Abated 6/19 Material Identified by MEC in 2012 |
| MMB | Fire Door | Boiler Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2012 |
| MMC | Exterior Window Glazing | Exterior Windows | N/A | N/A |  | Analyzed by True North to be ACM in 2018- Abated 6/19 Material Identified by MEC in 2012 |
| MCC | 2’x4’ Ceiling Tile- Small & Large Pin Holes | 201,202,203,204,208,211, Office Area | N/A | N/A |  | Analyzed by True North to be NON-ACM in 2018 Material Identified by True North in 2015 |
| MMD | Vibration Damper | Boiler Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2015 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.  NOTE:   If the status of the ACBM has changed, then photograph the area and record the photograph number in the space provided.  Notify the Asbestos Program Manager immediately concerning any changes.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 5 of 5

Building Name: Holy Family School

Building Address:   4407 Highcrest Road Rockford, Illinois 61107

Name of Person Completing Report:

Title:					                       				Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MFO? | 12”x12”Floor Tiles/Mastic-Blue | Room 109 Bathroom | ND | ND |  | Letter on File, NON-ACM-2018 |
| MCB? | Vinyl Wall Base/Mastic-Gray | Room 109 Bathroom | ND | ND |  | Letter on File, NON-ACM-2018 |
| MCD? | 2’x2’ Ceiling Tile-White | Room 109 Bathroom | ND | ND |  | Letter on File, NON-ACM-2018 |
| MME? | Drywall/Joint Compound | Room 109 Bathroom | ND | ND |  | Letter on File, NON-ACM-2018 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.  NOTE:   If the status of the ACBM has changed, then photograph the area and record the photograph number in the space provided.  Notify the Asbestos Program Manager immediately concerning any changes.