SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 1 of 4

Building Name:  Annunciation of the Blessed Virgin Mary

Building Address:  1840 Church Rd- Aurora, IL 60505

Name of Person Completing Report:

Title: 					                       				 Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 01 | 9”x 9”Floor Tile | Building #1-Throughout | See HA #11 | See HA #11 |  | HA# 01 has been Eliminated and is now Included w/HA# 11 |
| 02 | 12”x 12” Floor Tile/Mastic Tan w/Brown & White Streaks (Assumed to Remain under HA MFF) | Building #1-End of Hallway & Gym Perimeter | ND | ND |  | Tile Negative in 1988 by PLM-Both Tile and Mastic to remain ASSUMED- analyze Tile by TEM Method |
| 03 | Hard Plaster | Building #1-Gym Restrooms | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 04 | 3’x8’ Tectum Ceiling Decking | Building #1- Throughout | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 05 | Pipe Fitting Insulation | Building #1- Boiler Room, Gym, Hall Storage | ND | ND |  | Preventive Measures… Continue O&M Fittings abated BR on 3-15-2021 |
| 06 | 2’x4’ Lay-In Ceiling Tile- Deep Grooves | Building #2- Basement & 1st Floor | N/A | N/A |  | Only 2 samples in 1988- 3 Samples by MEC in December 2011- Analyzed to be NON-ACM |
| 07 | Spray-Applied Ceiling Fireproofing | Furnace Room & Mechanical Room | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| SPA | Plaster | Building #2- Basement & 1st Floor | N/A | N/A |  | HA #08- 29 Total samples by True North in July 2015 Analyzed Negative. |
| 09 | Gypsum Wall Board | Boiler Room | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 10 | 1’x1’ Acoustical Ceiling Tile | Basement Classroom | N/A | N/A |  | Material Analyzed to be NON-ACM in 1988 |
| 11 | 9”x 9” Floor Tile/Mastic- Tan w/Brown & White Marks | Building #1- Throughout (Below HA MFM) | ND | ND |  | Tile Negative in 1988 by PLM- Mastic Confirmed to be ACM by True North in 2014- Tile considered POSITIVE by Association JULY 2018 COVERED by HA MFM |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 2 of 4

Building Name:  Annunciation of the Blessed Virgin Mary

Building Address:  1840 Church Rd- Aurora, IL 60505

Name of Person Completing Report:

Title: 			                       				   		  Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 13 | Transite Panels | Building #2-2nd Floor Classroom Doors | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M |
| MCA | 2’X4’ Lay-In Ceiling Tile- Scattered Fissures | Building #2-Basement and 1st Floor | N/A | N/A |  | Incorrectly included with HA #6 in 1988- 3 Samples by MEC December 2011- Analyzed as NON-ACM |
| MBA | Vinyl Wall Base/Mastic- Tan | Building #2-Basement | N/A | N/A |  | Analyzed NEGATIVE June 2016 by True North Material Identified by MEC in 2011 Material Removed Summer 2016 |
| MFA | 12”x 12” Floor Tile/Mastic-Beige w/Green-Brown Flecks | Building #2- Basement | N/A | N/A |  | Analyzed NEGATIVE June 2016 by True North Material Identified by MEC in 2011 Material Removed Summer 2016 |
| MFB | 12”x 12” Floor Tile/Mastic- Light Blue Mottled | Building #2- Basement-Kitchen | N/A | N/A |  | Analyzed NEGATIVE June 2016 by True North Material Identified by MEC in 2011 Material Removed Summer 2016 |
| MFC | 12”x 12” Floor Tile/Mastic- Gray Mottled | Building #2- Basement | N/A | N/A |  | Analyzed NEGATIVE June 2016 by True North Material Identified by MEC in 2011 Material Removed Summer 2016 |
| MMA | Adhesive Puck- Associated with HA #10 | Building #2- Basement-Southwest Classroom | N/A | N/A |  | Sampled by MEC in December2011- Analyzed to be NON-ACM |
| MMB | Exterior Window Glazing | Building #2- Exterior-Entrances | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2011 |
| MBB | Vinyl Wall Base/Mastic- Black | Building #1- Throughout | ND | ND |  | Material analyzed Negative by True North Material Identified by MEC in 2011 REMOVED JULY 2018 |
| MBC | Vinyl Wall Base/Mastic- Gray | Building #1- Gym | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2011 |
| TPA | Paper Wrap Drain Pipe Insulation | Building #1- Boiler Room, Gym, Stage, Hallway Storage | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2011 |

*** Material Condition***       (ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 3 of 4

Building Name:  Annunciation of the Blessed Virgin Mary

Building Address:  1840 Church Rd- Aurora, IL 60505

Name of Person Completing Report:

Title:							                       		 Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MFD | 1” Ceramic Tile/Grout- Green, White and Gray | Building #1-Boys Bathroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2011 |
| MFE | 1” Ceramic Tile/Grout- Green, Beige and Light Green | Building #1-Girls Bathroom | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2011 |
| MFF | Linoleum- Blue | Building #1-Gymnasium | N/A | N/A |  | Abated June 2015 Material Identified by MEC in 2011 |
| MMC | Exterior Door Caulking | Building #1- Exterior Doors | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2011 |
| MMD | Exterior Window Caulking | Building #1- Exterior Windows | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2011 |
| MME | Exterior Transite Panel | Building #1- Exterior | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by MEC in 2011 |
| MFG | 9”x9” Floor Tile/Mastic- Brown w/White & Brown | Doorway #6 & #2, Stage Floor | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2014 |
| MFH | 9”x9” Floor Tile/Mastic-Gray w/Red & Black Streaks | Doorway #6 | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2014 |
| MFI | 12”x12” Floor Tile/Mastic- Black w/White Marks | Stage Floor in Gym | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2014 |
| MFJ | 12”x12” Floor Tile/Mastic- Gray w/Brown & White Marks | Middle of North Hallway | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2014 |
| MFK | Sheet Flooring- Brown Wood Pattern | Gym Floor | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2017 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management Office, attention Brian Heinkel, for insertion into our copy of your Asbestos Management Plan.  NOTE:   If the status of the ACBM has changed, then photograph the area and record the photograph number in the space provided.  Notify the Asbestos Program Manager immediately concerning any changes.

SIX MONTH ASBESTOS PERIODIC SURVEILLANCE REPORT				Page 4 of 4

Building Name:  Annunciation of the Blessed Virgin Mary

Building Address:  1840 Church Rd- Aurora, IL 60505

Name of Person Completing Report:

Title:						                       		                  Date:

| HA# | Material Description | Locations of material | Previous Condition *** | Current Condition *** | Photo # | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| MFL | Sheet Flooring- Blue | Gym Floor | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2017 |
| MMF | Vapor Barrier | Under Gym Floor | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2017 |
| MMG | Epoxy Floor Coating | Building 2- Basement, Kitchen, Lunch Room | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2017 |
| MFM | 18”x24” Vinyl Tile/Mastic | Building #1 Throughout, except Janitor Closet, Supply Closet, Storage Room | ND | ND |  | Installed Summer 2018 ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2020 |
| MBD | Vinyl Base – Gray | Building #1 Throughout, except Janitor Closet, Supply Closet, Storage Room | ND | ND |  | Installed Summer 2018 ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2020 |
| MFN | 12”X12” Floor Tile/Mastic- Lt. Brown with Grey | Building #1 in Janitor Closet (over HA #11) | ND | ND |  | ASSUMED- Preventive Measures… Continue O&M Material Identified by True North in 2020 |

*** Material Condition***

(ND)- Not Damaged          (D)- Damaged           (SD)- Significantly Damaged

The 6-month inspection must be performed and this form(s) completed by your AHERA-trained employee. Form(s) will be completed no later than March 30th and September 30th of each calendar year. The completed inspection form(s) should then be inserted into your Asbestos Management Plan.  A copy of the completed form must also be sent to the Diocesan Property Management.